## Slide 1: A naïve RISC-V CPU
January 4, 2020
Wu Runzhe

## Slide 2: Now let’s talk about the general design
A standard 5-stage pipeline with data forwarding

## Slide 3: Instruction Cache
No I-cache?
  5~6 cycles to fetch an instruction
  So pipeline what?
  Fake pipeline

## Slide 4: Instruction Cache
A direct mapping I-cache
  1,024 bytes
  256 instructions
Supports consecutive hits
  one instruction per cycle
A victim cache
  Sounds great
  But actually useless

## Slide 5: Data Cache
A direct mapping D-cache
  64 bytes
  Why so small
    useless

## Slide 6: Branch Prediction
Tournament Predictor
  Global Predictor & Local Predictor
  A selector
Branch Target Buffer
Predict at stage IF
Correct
  No stall
Incorrect
  Recover in stage EX by stalling 1 cycle

## Slide 7: Memory controller
To resolve structural hazard
Stage MEM priority over stage IF
Memory controller
Stage IF
Stage MEM
RAM

## Slide 8: Performance
130 MHz, all test cases passed
pi.c: 0.996875 s
When higher than 130 MHz, Bulgarian.c failed
  Because of the bad uart buffer?

## Slide 9: Now let’s focus on the details

## Slide 10: Victim cache

## Slide 11: Victim cache
A small and fully associative cache that stores all the blocks evicted from some cache
I don’t know why but it does little to reduce miss rate
Because I-cache is large enough
Speed up ≈ 1

## Slide 12: Victim cache

## Slide 13: Tournament Predictor
2 predictors: 1 based on global information and 1 based on local information, and combine with a selector
Global Predictor 4K entries, indexed by the history of the last 12 branches; each entry in the global predictor is a standard 2-bit saturating counter
Local Predictor 32 entries, indexed by the address of the branch instruction; each entry is a standard 2-bit saturating counter

## Slide 14: Tournament Predictor
Selector
  A 2-bit saturating counter
    0 stands for global predictor
    1 stands for local predictor
When a prediction produced by some predictor is correct, we should attach more importance to it.
Otherwise we should incline to the other predictor.

## Slide 15: Pipelined <-> Not pipelined
About debugging
A register named “avoid_data_hazard” to stall some specific cycles after an instruction is fetched in stage IF
“avoid_data_hazard” = 0
  Pipelined
“avoid_data_hazard” > 9
  Not pipelined

## Slide 16: Thank You!